FQM LIMITED

XXX-OP-014

Undocking a Vessel

- INSTRUCTIONS FOR UNDOCKING A VESSEL

- Vessel to be put back in same trim as docking.

- Four ropes and two wires must be connected to the bollards on ship before flooding the dock.

- Once the dock is flooded and the ship is floating the side shores will be removed.

- All services cables and hoses must be disconnected from shore side.

- The gangway will be removed on instructions from the Dock master.

- The aft ropes will then be slackened at the shore side and re-routed round the outermost bollard.

- The ships crew must NOT disconnect the rope from the ship at this time!

- The forward wires will then be slackened and the ships crew will then take the eye off the bits and then let the wire go into the dock.

- The dockside crew will then start to haul the ship aft towards the gate using our capstans and the dockside crew at the forward end will walk along the dock with the ships ropes.

- If required the dockside crew will put the forward ships mooring on a bollard to help centre the ship on the way out.

- Once the stern is over the gate the Ships Master has to get permission from Harbour Boards VTS to proceed.

- Once clearance has been given the Dock masters will instruct the ship to clutch in and move out of the dock.

- Once clutched in the aft two ropes are to be released from the ships bollards and pulled ashore.

- The two forward ships ropes will then be walked along the gate then the ships crew will pull them aboard.

- Note to Master:-

  - Leave dry dock using low speed as the wash can displace the blocks.