FQM LIMITED

XXX-OP-013

Dry Docking a Vessel

- Instructions for Dry Docking a Vessel at [COMPANY NAME]

- [COMPANY NAME] can be contacted on [TELEPHONE NUMBER] this number can also be used during out of office hours in the event of emergencies.

- You will only enter the dry-dock on the instructions of the Dock master xxxxx. In the event of emergencies he can be contacted on [TELEPHONE NUMBER].

- The ideal trim for entering the xxxxx dry-dock is 300mm down by the stern.

- The depth of our dry-dock is 1.9meters added onto the depth shown on the tide tables.

- When entering dry dock we require four ships mooring ropes long enough to reach our bollards at the side of the dock at least 20 meters from the side of your ship plus what is needed on deck to reach your windlass. Two rope forward (port & starboard) two ropes aft (port & starboard).

- You need sufficient crew to operate two ropes forward, and one person to take and relay instructions from the dock master to the crew members operating the mooring ropes.

- Sufficient crew will also be required to operate the aft mooring ropes, and one person to take and relay instructions from the dock master to the crew members operating the mooring ropes.

- When entering the dry dock we require the ship’s crew to throw two heaving lines from the bow, one port one starboard, connected to the ships mooring ropes.

- Our workers will walk up the dock side carrying the ropes.

- Give your engines a small kick ahead to move up the dock.

- Only use your thrusters for lining up with the dock.

- There is wooden fendering along the full length of the dock

- The Dales docking crew will then put the ropes on bollards and the ships crew will then pull the ship into dock using the ships windlass.

- Instructions for Dry Docking a Vessel at [SITE]

- We may have to use two extra mooring ropes if there is a strong side wind to hold the ship in position whilst we move the headlines and aft lines along the dock.

- Once the bow is in the dry dock do not use the bow thruster as this will knock over the blocks that will support your ship if you need to pull the ship to one side or the other instruct your deck crew to do this using your windlass.

- When your stern approaches the dock entrance we will require the ships crew to throw two heaving lines ashore aft connected to the ships mooring ropes one port one starboard.

- Finish with your engines once the two ropes are secure on the aft bollards. You must finish with engines not just clutch in or zero pitch the propellers as there is still a wash which can displace our blocks which support the ship.

- We then give you two wires forward which the crew put over the bollards taking care not to trap the forward mooring line as these may need to be altered to position the ship. Put the web sling over the bollards.

- When the ship comes to the final position in the dock the dock master will give instructions to the crew to hold the moorings fast.

- The dockside crane will then position the shores along the side of the ship

- We require ship’s crew to tie the shore ropes to the ship on the port and starboard sides.

- When the ship lands on the blocks, the pumps will be stopped and we will then hammer the shores up tight.

- Once the shores are secure we will start the pumps again and empty the dock.

- We will then crane the gangways into position, connect up the fire hose and any other services required.

- Please have someone on the bridge when the operation is taking place as we sometimes need to get crew assistance at different stages.