## Slide 1
Fire Warding Training
Introduction
Rev - April 2018

## Slide 2
Train employees to a level where
Fulfil role of fire warden
Respond to emergencies
Undertake routine fire safety procedures
Aims

## Slide 3
At the end of the course the participants will be able to :-
Describe the principles of fire initiation; classification and spread
Outline the principles of fire risk assessment
Describe the basic principles of fire prevention and prevention of fire in buildings
Identify appropriate fire alarm systems and fire fighting equipment in a simple building
Outline the factors to be considered when carrying out a successful evacuation of a building
Understand the basic legal requirements of fire prevention
Gain a more detailed understanding of the role of a Fire Warden or Fire Marshal
Objectives

## Slide 4
Fire wardens are nominated as a ‘competent person’ by an employer to
Take charge of an evacuation of a premises in the event of a fire
Undertake other specified duties as agreed with the employer
Very important role within any organisation
Responsible position – could save lives
Duties are either
Day to day
Reactive in the event of an emergency
Introduction
Notes: Size and type of buildings – multi-storey; out buildings etc

## Slide 5
Numbers of Fire Wardens depend upon
Size and type of building
Numbers of staff ( including any shift workers)
Remoteness of work areas
Cover required for sickness and holidays
Numbers usually identified through risk assessment
Introduction contd

## Slide 6
Numbers
35,000 fires at work in UK
30 Fatalities
Costs
Financial costs are high
40% businesses never start up again
Not to be underestimated!
1985 Bradford City Football Stadium
1987 Kings Cross Underground
2,500 injuries
Small fires can become infernos
Fire Statistics

## Slide 7
Since 1947 Fire Authority Responsibility
1971 Fire Precautions Act (FPA)
    Means of escape
    Basic fire protection equipment
    Fire certificates
    Only certain premises
1999 – Fire Precautions (Workplace) Regulations (FPWR)
    Wider range of premises
    Established principle of risk assessment
    Made under Health and Safety at Work Act (HASAWA)
Fire Legislation

## Slide 8
2005 Regulatory Reform (Fire Safety) Order (RRFSO)
    FPA repealed and FPWR revoked
    Move towards fire prevention
    Duty to ensure safety of employees
    Risk assessments
    Fire Authority Employers
Scotland - Fire is a devolved matter
    Fire (Scotland) Act 2005
    Fire Safety (Scotland) Regulations 2016
    Police & Fire Reform (Scotland) Act 2012
      Scottish Fire & Rescue Service
Fire Legislation 2

## Slide 9
7 General Categories
    Fire Safety Risk Assessment
    Identify fire safety measures
    Implement using risk reduction principles
    Initiate fire safety arrangements for control and review measures
    Comply with Fire Regulations
    Keep risk assessment under review
    Keep records (Fire Log Book)
Employer’s Duties

## Slide 10
Cannot occur unless three things present
Usually depicted as a fire triangle
Suggestions ?
Basic Principles of Fire

## Slide 11
    Naked flames
    External sparks
    Internal sparking
    Hot surfaces
    Static electricity
Sources of Ignition

## Slide 12
If it burns, it’s a fuel!
    Solids
    Liquids
    Gases
Sources of Fuel

## Slide 13
    Air (21% oxygen)
    Cylinders (e.g. welding)
    Certain chemicals containing oxygen
        Nitrates
        Phosphates
        Chlorates
Oxygen

## Slide 14
Five main classifications of fires.
How are they classified?
Extinguishers usually designed to tackle one or more classes of fires
Plus, electrical fires (provide source of ignition)
Class A
Solids - wood, paper, plastics, furnishings
Class B
Burning liquids - paint, oils, solvents
Class C
Gases, e.g. butane, propane
Class D
Burning metals
Class F
High temperature cooking oils and fats
Classifications of Fires

## Slide 15
Fires transmit heat in several ways. How?
Simple example …. Open fire; roasting potatoes, using metal fork; warming hands, feeling heat on your face
Convection - Hot air rises draws in cold air (with fresh oxygen) can ignite materials as it rises
Conduction - Through the material itself
good conductors – copper, steel, aluminium
poor conductors (insulators) – concrete, brickwork, asbestos
Radiation - Enough intensity to ignite adjacent surfaces or materials
Direct Contact - Catching fire through direct contact with flames
Heat Transmission / Fire Spread

## Slide 16
Fire & Smoke Spread in Buildings

## Slide 17
Fires in buildings (excluding dwellings) occurred in
Private garages and sheds (22%) 6700 fires
Retail distribution (14%) 4200 fires
Restaurants, cafes, pubs (9%) 2600 fires
Industrial (8%) 2400 fires
Recreational (6%) 1700 fires
Causes of Fires

## Slide 18
Deliberate (arson) 10,000
Faulty electrical appliances 5,000
Misuse of equipment 4,000
Accidental 3,800
Others 3,000
Anyone experienced a fire?
Caused by:-
Notes: OTHERS
Faulty fuel supplies
Chip pan fires
Careless handling of hot items
Articles close to hot surfaces
ACCIDENTAL
Cooking Appliances
Smoking Materials
Electrical Appliances

## Slide 19
Death
Real risk, but surprisingly low frequency
Overcome by gas or smoke 43%
Burns 26%
Burns and gas/smoke 20%
Personal injury - approx. 1,300 people
Building damage
Flora and fauna – forest and moorland fires
Loss of business and jobs
Underinsured
Not insured
Time and expense of restart
Environmental damage
Air pollution
Water pollution
Consequences

## Slide 20
Time for a Break!

## Slide 21
?
?
Questions

## Slide 22
Identify the Hazards (Fire Triangle)
    Any combustibles
    Sources of heat/ignition
        Normal use
        Carelessness
      Cooking
      Smoking materials
      Hot equipment / activities
      Electrical equipment
      Deliberate (arson)
    Unsafe Acts / Unsafe Conditions
      Smoking next to combustibles
      Open stairwells
      Polystyrene tiles
Comes under RRFSO - Basic five steps still apply
Fire Risk Assessment

## Slide 23
Identify Persons at Significant Risk
    Employees
    Visitors
    Contractors
    Special consideration or needs
    Young persons
Fire Risk Assessment 2

## Slide 24
Evaluate and Reduce Risks
    Use “principles of prevention”
      Eliminate
      Tackle at the source
      Replace dangerous by non dangerous
      Giving appropriate instructions
    Considering
      Fire detection and warning
      Means of escape
      Information signage
      Fire fighting arrangements
Risk is either Low
Normal – nearly all workplaces
High
Fire Risk Assessment 3

## Slide 25
Record Findings
    Date of assessment
    Hazards identified
    Staff or others at risk
    Produce action plan
    Recent conclusions
    Train staff
Fire Risk Assessment 4

## Slide 26
Monitor and Review Regularly
Significant changes in :-
    Occupancy
    Activities
    Materials used or stored
Fire Risk Assessment 5

## Slide 27
Consider
    Good housekeeping and storage
    Control of fuel sources
    Control of ignition sources
    Safe systems and procedures
Builds on the EVALUATION part of Risk Assessment
Good Housekeeping and Storage
    Reduces chances of blocked fire exits
    Reduces chances of concealing fire extinguishers and alarm points
    Waste kept in suitable containers and away from buildings
Fire Prevention / Preventing Fire Spread

## Slide 28
Control of Fuel Sources
    Correct storage and disposal especially oils, solvents, gas bottles and aerosols
    Substitute for less hazardous
Control of Ignition Sources
    Proper use, maintenance and testing or electrical items (fixed and portable)
    Good management of smoking areas
    Proper control over heating appliances
    Regular cleaning and maintenance of cooking equipment
Fire Prevention / Preventing Fire Spread contd

## Slide 29
Vital that everyone is alerted as soon as possible
Able to escape before fire takes hold
Should have some form of detector and warning system
Ranges from
Shout of “FIRE”
Whistles, gongs, klaxon, air horn
Fixed fire warning system
Call points and siren
Control panel
Should
Alert everyone
Be recognisable
Be heard in all locations
Need to have alternatives for people with hearing difficulties
Buddy system
Visual display / vibrating pager
Fire Detection and Alarm Systems

## Slide 30
Cooling
Reduces temperature
Takes heat out of the fire
water
Smothering
Limits oxygen availability
Prevents further combustion
Foam or fire blanket
Starvation
Limits fuel supply
Shutting gas supply off
Removing wood or paper etc.
Chemical reaction
Interrupts combustion
Chemical process involving chlorine and hydrogen
Used in Halon extinguishers
4 Main ways to extinguish fires
Fire Extinguishing Systems
Notes: Halon – Ozone depleting properties / environmental effects. No longer in general use. Specialist locations.

## Slide 31
Portable
    Syndicate Exercise
Two types :-
Fixed Installations
    Good for retail or warehouse premised
    High initial installation cost
    Possible stock damage from accidental release
Fire Extinguishing Systems contd

## Slide 32
Syndicate Slide

## Slide 33: Know your fire extinguishers
Know your Fire Extinguishers

## Slide 34
Know your Fire Extinguishers

## Slide 35
Includes
Detection and warning systems
Emergency lighting
Fire fighting equipment
Checked and maintained as per manufacturer’s recommendations
Records kept
Usually in a fire log book or similar
Whatever is installed or in place it must be available to respond in an emergency
Inspection, Maintenance & Testing of Fire Equip

## Slide 36
Essential that people can escape quickly
People need to turn away from a fire OR
Pass it when it is very small
Corridors may need protecting by self closing fire doors
Doors usually open in the direction of travel
Escape routes must be clear of obstructions particularly fire hazards
Escape routes need to be checked regularly
Escape routes must be well lit
Additional lighting may need to be provided on escape routes (torches, for example)
Exit signs with direction arrows should be provided on escape routes
Evactuation and Means of Escape

## Slide 37
Normally carried out via a Fire Action Notice
Fire Drills
Carried out to ensure staff know procedures
Normally done twice per year
Ensure all staff are covered
Names are recorded in Fire Log Book
Evacuation Procedures / Emergency Plans

## Slide 38: Fire Wardens – Day to Day Duties
Varies from company to company but could include:-
  Good standards of housekeeping maintained
  Exits/escape routes unobstructed
  Extinguishers/call points have good access
  Smoking rules enforced
  Staff are trained in use of fire equipment
  Emergency lighting tested monthly
  Fire alarms are tested weekly
  Assist in review of risk assessment
  Ensure electrical checks are carried out
  Ensure all documentation is filed and up to date
Fire Wardens – Day to Day Duties

## Slide 39: Fire Wardens – Emergency Situations
  Take charge in the event of an emergency
  Varies from company to company, but –
    Fight fire, if safe to do so
    Ensure alarm is raised
    Ensure all locations have been evacuated
    Fire and Rescue Service contacted
    Fire doors and windows are closed
    Equipment shut down if safe to do so
    Roll call is carried out at the Assembly Point
    Ensure persons with special needs are covered
    Report to Fire and Rescue Service on their arrival
Fire Wardens – Emergency Situations

## Slide 40
At the end of the course the participants will be able to :-
Describe the principles of fire initiation; classification and spread
Outline the principles of fire risk assessment
Describe the basic principles of fire prevention and prevention of fire in buildings
Identify appropriate fire alarm systems and fire fighting equipment in a simple building
Outline the factors to be considered when carrying out a successful evacuation of a building
Understand the basic legal requirements of fire prevention
Gain a more detailed understanding of the role of a Fire Warden or Fire Marshal
Objectives