| Task Description |  | RA Number (if required) |
| --- | --- | --- |
| General workshop activities including public enquiries and delivery of materials and goods. (Risk Assessment name based on activity description) |  | ??? |

| Hazard | Activity | Initial Risk (No Controls) | Controls | Residual Risk (With Controls) |
| --- | --- | --- | --- | --- |
| Description | Population at Risk | Harm Effect |  | L | C | R | List all Controls Required | L | C | R |
| Moving vehicles | Public and visitors Contractors Staff | Injury from impact with vehicle | 1. Forklift operations | 3 | 5 | 15 | 1. a) Segregate forklift operations from public access area 1 b) Staff and contractors to wear high viz | 2 | 5 | 10 |
|  | Contractors Staff | Injury from impact with vehicle | 1. Customer vehicles reversing into premises | 3 | 2 | 6 | 1. a) Use banksman to control customer vehicle reversing 1. b) Staff and contractors to wear high viz | 2 | 2 | 4 |
| Powered machines | Public and visitors Contractors Staff | Injury from entrapment in machinery | 1. Unauthorised access to area 2. Working on machinery and equipment 3. Use of machinery and equipment | 4 | 4 | 16 | 1. a) Segregate public from workshop 1. b) Erect signage to prohibit unauthorised access. 2. All contractors to work under risk assessment and method statement 3. Only trained and authorised staff to operate machinery and equipment as per design intent and manufacturer’s instructions | 2 | 4 | 8 |
| Power supplies | Contractors | Electrocution from power supplies | 1. Working on machinery and equipment | 3 | 5 | 15 | 1. All contractors to work under risk assessment and method statement to specifically include isolation procedures | 1 | 5 | 5 |
|  | Staff | Electrocution from damaged power supplies | 1. Use of machinery | 3 | 5 | 15 | 1. a) PAT and FAT checks to be performed on a regular basis where required 1. b) Only trained and authorised staff to operate machinery and equipment as per design intent and manufacturer’s instructions including pre use checks | 2 | 5 | 10 |
| Slips, trips and falls | Public and visitors Contractors Staff | Injury from falls | 1. Moving around the area | 2 | 4 | 8 | 1. a) Segregate public access area from NFMS 1. b) Erect signage to prohibit unauthorised access. 2. a) All contractors to work under risk assessment and method statement to include housekeeping 2. b) All contractors to be given a site induction 3. All staff to maintain good housekeeping standards | 2 | 2 | 4 |
| Sharp objects Contamination | Public and visitors Contractors Staff | Cuts and abrasions from sharp and contaminated tools and materials | 1. Unauthorised access to area 2. Working on machinery and equipment 3. Use of machinery and equipment | 4 | 3 | 12 | 1. a) Segregate public access area from workshop 1. b) Erect signage to prohibit unauthorised access. 2. a) All contractors to work under risk assessment and method statement to include minimum PPE requirements 3. All staff to observe and monitor compliance with minimum PPE requirements for workshop area i.e Gloves to EN388, boots to EN 345-1 and high vis 4. Vermin to be tightly controlled by specialist contractor | 2 | 1 | 2 |

| Assessed By (please list all involved in initial assessment) | Location | Date | Time |
| --- | --- | --- | --- |
| Reviewed By (please list all involved in subsequent assessment reviews) | Location | Date | Time |

|  |  | LIKELIHOOD |
| --- | --- | --- |
|  | Hazard Severity | Environment | People | 1 Very unlikely A freak combination of factors required for incident to result | 2 Unlikely An unusual combination of factors would be required for an incident to result | 3 Possible Could happen with some additional factors present but otherwise unlikely to occur | 4 Likely Not certain to happen but a few additional factor may result in an accident | 5 Very Likely Almost inevitable that an incident would result |
| CONSEQUENCE Likelihood | 1 Slight | Little or no actual potential for damage. | Slight health effect/injury (Site First Aid) | 1 | 2 | 3 | 4 | 5 |
|  | 2 Minor | Within site boundary, short term impact recoverable by the work site | Minor health effect/ injury (A&E treatment) RWC LTI | 2 | 4 | 6 | 8 | 10 |
|  | 3 Major | Beyond the site boundary unlikely to last Beyond 1 month. Recovery may require external aid. | Major health effect/ injury Hospitalisation LTI DAFWC RIDDOR reportable | 3 | 6 | 9 | 12 | 15 |
|  | 4 Severe | Beyond the site boundary unlikely to last beyond 12 months. Recovery requires external aid. | Serious health effect/injury leading to partial or total disability | 4 | 8 | 12 | 16 | 20 |
|  | 5* Catastrophic | Uncontrolled release with significant impact extending well beyond the site boundary. | Fatality | 5* | 10 | 15 | 20 | 25 |

| Green (Low) | Risk is acceptable. Monitor for any changes and review to schedule. |
| --- | --- |
| Yellow (Medium) | Some risk still present. Task should only proceed with appropriate management authorisation and close monitoring. Specialist support and assessment may be required. Consider reviewing task to seek alternative options or further control measures to be put in place to reduce risk. |
| Red (High) | Intolerable. Task must not proceed. Task must be reviewed to consider alternative options or further control measures put in place to reduce risk. The controls must be re-assessed for adequacy prior to task commencement. |

This matrix is only intended to cover two different types of risk.

People –harm to individuals through injury or damage to health

Environment – damage to the environment (commonly through a spill or release)